## Slide 1: Unit-5 Central Processing Unit

## Slide 2

Looping
Outline
  General Register Organization
  Stack Organization
  Instruction format
  Addressing Modes
  Data transfer and manipulation
  Program Control
  Reduced Instruction Set Computer (RISC)
  Complex Instruction Set Computer (CISC)

## Slide 3: General Register Organization
Section - 1

## Slide 4
R1
R2
R3
R4
R5
R6
R7
MUX - A
MUX - B
Arithmetic Logic Unit
(ALU)
3x8
decoder
Clock
Input
Output
SEL B
SEL A
SEL D
OPR
Load
(7 lines)
A - bus
B - bus

## Slide 5: General Register Organization
Example: R1 R2 + R3
To perform the above operation, the control must provide binary selection variables to the following selector inputs:
MUX A selector (SELA): to place the content of R2 into bus A.
MUX B selector (SELB): to place the content of R3 into bus B.
ALU operation selector (OPR): to provide the arithmetic addition A + B.
Decoder destination selector (SELD): to transfer the content of the output bus into R1.
Control Word:
SELA
SELB
SELD
OPR

## Slide 6: General Register Organization
Binary Code | SELA | SELB | SELD
000 | Input | Input | None
001 | R1 | R1 | R1
010 | R2 | R2 | R2
011 | R3 | R3 | R3
100 | R4 | R4 | R4
101 | R5 | R5 | R5
110 | R6 | R6 | R6
111 | R7 | R7 | R7
OPR Select | Operation | Symbol
00000 | Transfer A | TSFA
00001 | Increment A | INCA
00010 | A + B | ADD
00101 | A – B | SUB
00110 | Decrement A | DECA
01000 | A and B | AND
01010 | A or B | OR
01100 | A xor B | XOR
01110 | Complement A | COMA
10000 | Shift right A | SHRA
11000 | Shift left A | SHLA
Encoding of Register Selection Fields
Encoding of ALU Operations

## Slide 7: Stack Organization
Section - 2

## Slide 8: Stack Organization
A stack is a storage device that stores information in such a manner that the item stored last is the first item retrieved (LIFO).
The register that holds the address for the stack is called a stack pointer (SP) because its value always points at the top item in the stack.
The physical registers of a stack are always available for reading or writing. It is the content of the word that is inserted or deleted.
There are two types of stack organization
  Register stack – built using registers
  Memory stack – logical part of memory allocated as stack

## Slide 9: Register Stack
PUSH Operation
C
B
A
DR
FULL
EMPTY
SP
63
3
2
1
0
4
Address
SP ← SP + 1
M[SP] ← DR
IF (SP= 0) then (FULL ← 1)
EMTY ← 0
DR ← M[SP]
SP ← SP - 1
IF (SP= 0) then (EMTY ← 1)
FULL ← 0
POP Operation

## Slide 10: Register Stack
A stack can be placed in a portion of a large memory or it can be organized as a collection of a finite number of memory words or registers. Figure shows the organization of a 64-word register stack.
The stack pointer register SP contains a binary number whose value is equal to the address of the word that is currently on top of the stack.
In a 64-word stack, the stack pointer contains 6 bits because 26 = 64.
Since SP has only six bits, it cannot exceed a number greater than 63 (111111 in binary).
The one-bit register FULL is set to 1 when the stack is full, and the one-bit register EMTY is set to 1 when the stack is empty of items.
DR is the data register that holds the binary data to be written into or read out of the stack.

## Slide 11: Memory Stack
PUSH Operation
SP ← SP - 1
M[SP] ← DR
DR ← M[SP]
SP ← SP + 1
POP Operation
Program
(instructions)
Data
(operands)
Stack
DR
1000
Address
2000
3000
3997
3998
3999
4000
4001
PC
AR
SP

## Slide 12: Memory Stack
The implementation of a stack in the CPU is done by assigning a portion of memory to a stack operation and using a processor register as a stack pointer.
Figure shows a portion of computer memory partitioned into three segments: program, data, and stack.
The program counter PC points at the address of the next instruction in the program which is used during the fetch phase to read an instruction.
The address registers AR points at an array of data which is used during the execute phase to read an operand.
The stack pointer SP points at the top of the stack which is used to push or pop items into or from the stack.
We assume that the items in the stack communicate with a data register DR.

## Slide 13: Reverse Polish Notation
The common mathematical method of writing arithmetic expressions imposes difficulties when evaluated by a computer.
The Polish mathematician Lukasiewicz showed that arithmetic expressions can be represented in prefix notation as well as postfix notation.
A + B
+ AB
AB +
Infix
Prefix or Polish
Postfix or Reverse Polish
A * B + C * D
AB * CD * +
Reverse Polish

## Slide 14: Evaluation of Arithmetic Expression
(3 * 4) + (5 * 6)
3 4 * 5 6 * +
3
4
3
12
5
12
6
5
12
30
12
42
3
4
*
5
6
*
+
42

## Slide 15: Instruction format
Section - 3

## Slide 16: Instruction Formats
Instructions are categorized into different formats with respect to the operand fields in the instructions.
Three Address Instructions
Two Address Instruction
One Address Instruction
Zero Address Instruction
RISC Instructions

## Slide 17: Three Address Instruction
Computers with three-address instruction formats can use each address field to specify either a processor register or a memory operand.
The program in assembly language that evaluates X = (A + B) * (C + D) is shown below.
The advantage of three-address format is that it results in short programs when evaluating arithmetic expressions.
The disadvantage is that the binary-coded instructions require too many bits to specify three addresses.
ADD R1, A, B
R1← M[A]+ M[B]
ADD R2, C, D
R2← M[C]+ M[D]
MUL X, R1, R2
M[X]← R1 * R2

## Slide 18: Two Address Instruction
Two address instructions are the most common in commercial computers. Here again each address field can specify either a processor register or a memory word.
The program to evaluate X = (A + B) * (C + D) is as follows:
MOV R1, A
R1← M[A]
ADD R1, B
R1← R1+ M[B]
MOV R2, C
R2← M[C]
ADD R2, D
R2← R2+ M[D]
MUL R1, R2
R1← R1 * R2
M[X]← R1
MOV X, R1

## Slide 19: One Address Instruction
One address instructions use an implied accumulator (AC) register for all data manipulation.
For multiplication and division these is a need for a second register.
However, here we will neglect the second register and assume that the AC contains the result of all operations.
The program to evaluate X = (A + B) * (C + D) is
LOAD A
AC← M[A]
ADD B
AC← AC+M[B]
STORE T
M[T]←AC
LOAD C
AC← M[C]
ADD D
AC← AC+M[D]
MUL T
AC← AC*M[T]
STORE X
M[X]←AC

## Slide 20: Zero Address Instruction
A stack-organized computer does not use an address field for the instructions ADD and MUL.
The PUSH and POP instructions, however, need an address field to specify the operand that communicates with the stack.
The program to evaluate X = (A + B) * (C + D) will be written for a stack-organized computer.
To evaluate arithmetic expressions in a stack computer, it is necessary to convert the expression into reverse polish notation.
PUSH A
TOS← M[A]
PUSH B
TOS← M[B]
ADD
TOS←(A+B)
PUSH C
TOS← M[C]
PUSH D
TOS← M[D]
ADD
TOS←(C+D)
MUL
TOS←(C+D)*(A+B)
POP X
M[X] ← TOS

## Slide 21: RISC Instruction
The instruction set of a typical RISC processor is restricted to the use of load and store instructions when communicating between memory and CPU.
All other instructions are executed within the registers of the CPU without referring to memory.
A program for a RISC type CPU consists of LOAD and STORE instructions that have one memory and one register address, and computational-type instructions that have three addresses with all three specifying processor registers.
The following is a program to evaluate X = (A + B) * (C + D)
LOAD R1, A
R1← M[A]
LOAD R2, B
R2← M[B]
LOAD R3, C
R3← M[C]
LOAD R4, D
R4← M[D]
ADD R1, R1, R2
R1← R1+R2
ADD R3, R3, R4
R3← R3+R4
MUL R1, R1, R3
R1← R1*R3
STORE X, R1
M[X] ← R1

## Slide 22: Addressing Modes
Section - 4

## Slide 23: Addressing Modes
The addressing mode specifies a rule for interpreting or modifying the address field of the instruction before the operand is actually referenced.
Computers use addressing mode techniques for the purpose of accommodating one or both of the following provisions:
  To give programming versatility to the user by providing such facilities as pointers to memory, counters for loop control, indexing of data, and program relocation.
  To reduce the number of bits in the addressing field of the instruction.
There are basic 10 addressing modes supported by the computer.
Implied Mode
Immediate Mode
Register Mode
Register Indirect Mode
Autoincrement or Autodecrement Mode
Direct Address Mode
Indirect Address Mode
Relative Address Mode
Indexed Addressing Mode
Base Register Addressing Mode

## Slide 24: 1. Implied Mode & 2. Immediate Mode
Operands are specified implicitly in the definition of the instruction.
For example, the instruction “complement accumulator (CMA)” is an implied-mode instruction because the operand in the accumulator register is implied in the definition of the instruction.
In fact, all register reference instructions that use an accumulator and zero address instructions are implied mode instructions.
Operand is specified in the instruction itself.
In other words, an immediate-mode instruction has an operand field rather than an address field.
The operand field contains the actual operand to be used in conjunction with the operation specified in the instruction.
Immediate mode of instructions is useful for initializing register to constant value.
E.g. MOV R1, 05H
instruction copies immediate number 05H to R1 register.
1. Implied Mode
2. Immediate Mode

## Slide 25: 3. Register Mode & 4. Register Indirect Mode
Operands are in registers that reside within the CPU.
The particular register is selected from a register field in the instruction.
E.g. MOV AX, BX
move value from BX to AX register
In this mode the instruction specifies a register in the CPU whose contents give the address of the operand in memory.
Before using a register indirect mode instruction, the programmer must ensure that the memory address of the operand is placed in the processor register with a previous instruction.
The advantage of this mode is that address field of the instruction uses fewer bits to select a register than would have been required to specify a memory address directly.
E.g. MOV [R1], R2
value of R2 is moved to the memory location specified in R1.
3. Register Mode
4. Register Indirect Mode

## Slide 26: 5. Autoincrement or Autodecrement Mode & 6. Direct Address Mode
This is similar to the register indirect mode expect that the register is incremented or decremented after (or before) its value is used to access memory.
When the address stored in the register refers to a table of data in memory, it is necessary to increment or decrement the register after every access to the table. This can be achieved by using the increment or decrement instruction.
In this mode the effective address is equal to the address part of the instruction.
The operand resides in memory and its address is given directly by the address field of the instruction.
E.g. ADD 457
5. Autoincrement or Autodecrement Mode
6. Direct Address Mode

## Slide 27: 7. Indirect Address Mode & 8. Relative Address Mode
In this mode the address field of the instruction gives the address where the effective address is stored in memory.
Control fetches the instruction from memory and uses its address part to access memory again to read the effective address.
The effective address in this mode is obtained from the following computational:
Effective address = address part of instruction + content of CPU register
In this mode the content of the program counter is added to the address part of the instruction in order to obtain the effective address.
The address part of the instruction is usually a signed number which can be either positive or negative.
Effective address = address part of instruction + content of PC
7. Indirect Address Mode
8. Relative Address Mode

## Slide 28: 9. Indexed Addressing Mode & 10. Base Register Addressing Mode
In this mode the content of an index register is added to the address part of the instruction to obtain the effective address.
The indexed register is a special CPU register that contain an index value.
The address field of the instruction defines the beginning address of a data array in memory.
Each operand in the array is stored in memory relative to the begging address.
Effective address = address part of instruction + content of index register
In this mode the content of a base register is added to the address part of the instruction to obtain the effective address.
A base register is assumed to hold a base address and the address field of the instruction gives a displacement relative to this base address.
The base register addressing mode is used in computers to facilitate the relocation of programs in memory.
Effective address = address part of instruction + content of base register
9. Indexed Addressing Mode
10. Base Register Addressing Mode

## Slide 29: Data transfer and manipulation
Section - 5

## Slide 30: Data transfer instructions
Data transfer instructions move data from one place in the computer to another without changing the data content.
The most common transfers are between memory and processor registers, between processor registers and input or output, and between the processor registers themselves.
Name | Mnemonic
Load | LD
Store | ST
Move | MOV
Exchange | XCH
Input | IN
Output | OUT
Push | PUSH
Pop | POP
The data manipulation instructions in a typical computer are usually divided into three basic types:
  Arithmetic instructions
  Logical and bit manipulation instructions
  Shift instructions

## Slide 31: Instructions
Name | Mnemonic
Increment | INC
Decrement | DEC
Add | ADD
Subtract | SUB
Multiply | MUL
Divide | DIV
Add with carry | ADDC
Subtract with borrow | SUBB
Negate (2’s complement) | NEG
Name | Mnemonic
Clear | CLR
Complement | COM
AND | AND
OR | OR
Exclusive-OR | XOR
Clear carry | CLRC
Set carry | SETC
Complement carry | COMC
Enable interrupt | EI
Disable interrupt | DI
Name | Mnemonic
Logical shift right | SHR
Logical shift left | SHL
Arithmetic shift right | SHRA
Arithmetic shift left | SHLA
Rotate right | ROR
Rotate left | ROL
Rotate right through carry | RORC
Rotate left through carry | ROLC
Arithmetic Instructions
Logical & Bit Manipulation Instructions
Shift Instructions

## Slide 32: Program Control
Section - 6

## Slide 33: Program Control
A program control type of instruction, when executed, may change the address value in the program counter and cause the flow of control to be altered.
The change in value of the program counter as a result of the execution of a program control instruction causes a break in the sequence of instruction execution.
Name | Mnemonic
Branch | BUN
Jump | JMP
Skip | SKP
Call | CALL
Return | RET
Compare (by subtraction) | CMP
Test (by ANDing) | TST

## Slide 34: Status Bit Conditions
Bit C (carry) is set to 1 if the end carry C8 is 1. It is cleared to 0 if the carry is 0.
Bit S (sign) is set to 1 if the highest-order bit F7 is 1. It is set to 0 if the bit is 0.
Bit Z (zero) is set to 1 if the output is zero and Z = 0 if the output is not zero.
Bit V (overflow) is set to 1 if the exclusive-OR of the last two carries is equal to 1, and cleared to 0 otherwise. This is the condition for an overflow when negative numbers are in 2’s complement.
8-bit ALU
A
B
8
8
V | Z | S | C
Check for zero output
8
Output F

## Slide 35: Program Interrupt
The interrupt procedure is, in principle, quite similar to a subroutine call except for three variations:
  The interrupt is usually initiated by an internal or external signal rather than from the execution of an instruction
  The address of the interrupt service program is determined by the hardware rather than from the address field of an instruction
  An interrupt procedure usually stores all the information necessary to define the state of the CPU rather than storing only the program counter.
After a program has been interrupted and the service routine been executed, the CPU must return to exactly the same state that it was when the interrupt occurred. Only if this happens will the interrupted program be able to resume exactly as if nothing had happened.
The state of the CPU at the end of the execute cycle (when the interrupt is recognized) is determined from:
  The content of the program counter
  The content of all processor registers
  The content of certain status conditions

## Slide 36: Types of interrupts
There are three major types of interrupts that cause a break in the normal execution of a program. They can be classified as:
  External interrupts
  Internal interrupts
  Software interrupts

## Slide 37: 1. External Interrupt
External interrupts come from
  Input-output (I/O) devices
  Timing device
  Circuit monitoring the power supply
  Any other external source
Examples that cause external interrupts are
  I/O device requesting transfer of data
  I/O device finished transfer of data
  Elapsed time of an event
  Power failure
External interrupts are asynchronous.
External interrupts depend on external conditions that are independent of the program being executed at the time.

## Slide 38: 2. Internal interrupts (Traps)
Internal interrupts arise from
  Illegal or erroneous use of an instruction or data.
Examples of interrupts caused by internal error conditions like
  Register overflow
  Attempt to divide by zero
  invalid operation code
  stack overflow
  protection violation.
These error conditions usually occur as a result of a premature termination of the instruction execution.
Internal interrupts are synchronous with the program. If the program is rerun, the internal interrupts will occur in the same place each time.

## Slide 39: 3. Software interrupts
A software interrupt is a special call instruction that behaves like an interrupt rather than a subroutine call.
The most common use of software interrupt is associated with a supervisor call instruction. This instruction provides means for switching from a CPU user mode to the supervisor mode.
When an input or output transfer is required, the supervisor mode is requested by means of a supervisor call instruction. This instruction causes a software interrupt that stores the old CPU state and brings in a new PSW that belongs to the supervisor mode.
The calling program must pass information to the operating system in order to specify the particular task requested.

## Slide 40: Reduced Instruction Set Computer (RISC)
Section - 7

## Slide 41: Reduced Instruction Set Computer (RISC)
Characteristics of RISC are as follows:
  Relatively few instructions
  Relatively few addressing modes
  Memory access limited to load and store instructions
  All operations done within the registers of the CPU
  Fixed-length, easily decoded instruction format
  Single-cycle instruction execution
  Hardwired rather than microprogrammed control
  A relatively large number of registers in the processor unit
  Use of overlapped register windows to speed-up procedure call and return
  Efficient instruction pipeline
  Compiler support for efficient translation of high-level language programs into machine language programs

## Slide 42: Overlapped Register Window
A characteristic of some RISC processors is their use of overlapped register windows to provide the passing of parameters and avoid the need for saving and restoring register values.
Each procedure call results in the allocation of a new window consisting of a set of registers from the register file for use by the new procedure.
R15
R10
R73
R64
R63
R58
R57
R48
R47
R42
R41
R32
R31
R26
R25
R16
R15
R10
R9
R0
Global registers
Common to all procedures
Common to D and A
Local to D
Common to C and D
Common to B and C
Common to A and B
Common to A and D
Local to C
Local to B
Local to A
Proc A
Proc D
Proc C
Proc B
Window size = L + 2C + G
Register file = (L + C) W + G

## Slide 43: Complex Instruction Set Computer (CISC)
Section - 8

## Slide 44: Complex Instruction Set Computer (CISC)
Characteristics of CISC are as follows:
  A larger number of instructions – typically from 100 to 250 instructions
  Some instructions that perform specialized tasks and are used infrequently
  A large variety of addressing modes – typically from 5 to 20 different modes
  Variable-length instruction formats
  Instructions that manipulate operands in memory