## Slide 1: Unit-7 Computer Arithmetic

## Slide 2

Looping
Outline
  Addition and Subtraction
  Multiplication Algorithms (Booth Multiplication Algorithm)
  Decimal Arithmetic Unit

## Slide 3: Addition and Subtraction
Section - 1

## Slide 4: Addition and Subtraction
Operation | Add Magnitudes | Subtract Magnitudes |  | 
 |  | When A > B | When A < B | When A = B
(+A) + (+B) | + (A + B) |  |  | 
(+A) + (-B) |  | + (A - B) | - (B - A) | + (A - B)
(-A) + (+B) |  | - (A - B) | + (B - A) | + (A - B)
(-A) + (-B) | - (A + B) |  |  | 
(+A) - (+B) |  | + (A - B) | - (B - A) | + (A - B)
(+A) - (-B) | + (A + B) |  |  | 
(-A) - (+B) | - (A + B) |  |  | 
(-A) - (-B) |  | - (A - B) | + (B - A) | + (A - B)

## Slide 5: Flowchart for Addition & Subtraction
Subtract operation
Add operation
Minuend in A
Subtrahend in B
Augend in A
Addend in B
As⊕Bs
As⊕Bs
EA ← A+B’+1
AVF ← 0
EA ← A+B
E
AVF ← E
A ← A’
A
A ← A+1
As ← As’
As ← 0
END
(result is in A and As)
= 0
= 1
= 1
= 0
As = Bs
As = Bs
As ≠ Bs
As ≠ Bs
= 0
= 1
A < B
A ≥ B
≠ 0
= 0
As = Sign bit of A
Bs = Sign bit of B
AVF = add overflow flip-flop
E = Carry

## Slide 6: Multiplication Algorithms (Booth Multiplication Algorithm)
Section - 2

## Slide 7: Multiplication
Traditional way of binary multiplication
23
19
10111
10011
x
x
10111
10111
00000
00000
10111
110110101
437
Multiply operation
= 1
= 0
SC
= 0
≠ 0
Multiplicand in B Multiplier in Q
END
(PRODUCT is in AQ)

## Slide 8: Perform 23 x 19
Multiplicand B = 10111 | E | A | Q | SC
Multiplier in Q | 0 | 00000 | 10011 | 101
Qn = 1; add B |  | 10111 |  | 
First partial product | 0 | 10111 |  | 
Shift right EAQ | 0 | 01011 | 11001 | 100
Qn = 1; add B |  | 10111 |  | 
Second partial product | 1 | 00010 |  | 
Shift right EAQ | 0 | 10001 | 01100 | 011
Qn = 0; shift right EAQ | 0 | 01000 | 10110 | 010
Qn = 0; shift right EAQ | 0 | 00100 | 01011 | 001
Qn = 1; add B |  | 10111 |  | 
Fifth partial product | 0 | 11011 |  | 
Shift right EAQ | 0 | 01101 | 10101 | 000
Final product in AQ = 0110110101 |  |  |  | 

## Slide 9: Multiply (-9) x (-13) using Booth Algorithm
 |  | = 10111 = 01001 |  |  |  | 
 |  | Initial | 00000 | 10011 | 0 | 101
1 | 0 | Subtract BR | 01001 |  |  | 
 |  |  | 01001 |  |  | 
 |  | ashr | 00100 | 11001 | 1 | 100
1 | 1 | ashr | 00010 | 01100 | 1 | 011
0 | 1 | Add BR | 10111 |  |  | 
 |  |  | 11001 |  |  | 
 |  | ashr | 11100 | 10110 | 0 | 010
0 | 0 | ashr | 11110 | 01011 | 0 | 001
1 | 0 | Subtract BR | 01001 |  |  | 
 |  |  | 00111 |  |  | 
 |  | ashr | 00011 | 10101 | 1 | 000
 |  | Initial | 00000 | 10011 | 0 | 101
1 | 0 | Subtract BR | 01001 |  |  | 
 |  |  | 01001 |  |  | 
 |  | ashr | 00100 | 11001 | 1 | 100
1 | 1 | ashr | 00010 | 01100 | 1 | 011
0 | 1 | Add BR | 10111 |  |  | 
 |  |  | 11001 |  |  | 
 |  | ashr | 11100 | 10110 | 0 | 010
0 | 0 | ashr | 11110 | 01011 | 0 | 001
1 | 0 | Subtract BR | 01001 |  |  | 
 |  |  | 00111 |  |  | 
 |  | ashr | 00011 | 10101 | 1 | 000

## Slide 10: Booth Multiplication Algorithm
Multiply operation
= 01
= 10
SC
= 0
≠ 0
Multiplicand in BR Multiplier in QR
END
= 00
= 11

## Slide 11: Decimal Arithmetic Unit
Section - 3

## Slide 12: BCD Adder
Two BCD digits are applied to 4-bit binary adder which produce result ranging from 0 to 19 i.e. 9 + 9 + 1 = 19
Output sum of two decimal numbers must be represented in BCD.
Problem is to find rule by which binary number is to be converted to correct BCD
1001
0111
+
97
99
+
196
Both groups generate carry
1001
1001
0011
0000
+0110
+0110
1001
0110
Add 0110 to each
1
1
1
If codes are illegal or carry is generated in the group then we add 0110 to that particular group

## Slide 13: BCD Adder
Binary Sum |  |  |  |  | BCD Sum |  |  |  |  | 
K | Z8 | Z4 | Z2 | Z1 | C | S8 | S4 | S2 | S1 | Decimal
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 2
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 3
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 4
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 5
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 6
0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 7
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 8
0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 9
Binary Sum |  |  |  |  | BCD Sum |  |  |  |  | 
K | Z8 | Z4 | Z2 | Z1 | C | S8 | S4 | S2 | S1 | Decimal
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 10
0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 11
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 12
0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 13
0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 14
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 15
1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 16
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 17
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 18
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 19

## Slide 14: BCD Adder
Correction from binary to BCD is needed in following conditions
  K = 1
  Z8 and Z4 or Z8 and Z2 must have 1
4-bit binary adder
Z8 Z4 Z2 Z1
K
4-bit binary adder
Addend
Augend
0
Carry out
Output carry
S8 S4 S2 S1
Carry in