## Slide 1: Unit-8 Input-Output Organization
Computer Organization & Architecture (COA)
GTU # 3140707

## Slide 2

Looping
Outline
  Asynchronous Data Transfer
  Modes Of Transfer
  Priority Interrupt
  DMA
  Input-Output Processor (IOP)

## Slide 3: Asynchronous Data Transfer
Section - 1

## Slide 4: Asynchronous Data Transfer
Asynchronous data transfer between two independent units requires that control signals be transmitted between the communicating units to indicate the time at which data is being transmitted.
Two ways of achieving
  Strobe
  Handshaking

## Slide 5: Strobe Method
1.1 Source initiated Strobe
Source unit
Destination unit
Data Bus
Strobe
Valid Data
Data
Strobe
1.2 Destination initiated Strobe
Source unit
Destination unit
Data Bus
Strobe
Valid Data
Data
Strobe

## Slide 6: 2.1 Source initiated Handshake
Source unit
Destination unit
Data bus
Data valid
Valid Data
Data bus
Data accepted
Data accepted
Data valid
Place data on bus.
Enable data valid.
Accept data from bus.
Enable data accepted.
Disable data valid.
Invalidate data on bus.
Disable data accepted.
Ready to accept data (initial state).
Source unit
Destination unit

## Slide 7: 2.2 Destination initiated Handshake
Source unit
Destination unit
Data bus
Data valid
Ready for data
Ready for data
Data valid
Data bus
Valid Data
Place data on bus.
Enable data valid.
Ready to accept data.
Enable Ready for data.
Source unit
Destination unit
Accept data from bus.
Disable Ready for data.
Disable data valid.
Invalid data on bus
(initial state).

## Slide 8: Asynchronous Serial Transfer
Rules for transmission
  When a character is not being sent, the line is kept in the 1-state.
  The initiation of a character transmission is detected from the start bit, which is always 0.
  The character bits always follow the start bit.
  After the last bit of the character is transmitted, a stop bit is detected when the line returns to the 1-state for at least one bit time.
Start
bit
Stop
bits
Character bit
1
1
0
0
0
1
0
1

## Slide 9: Modes Of Transfer
Section - 2

## Slide 10: Modes of Transfer
Data transfer between the central computer and I/O devices may be handled in a variety of modes.
Some modes use the CPU as an intermediate path; others transfer the data directly to and from the memory unit.
Data transfer to and from peripherals may be handled in one of three possible modes:
  Programmed I/O
  Interrupt-initiated I/O
  Direct memory access (DMA)

## Slide 11: Programmed I/O
CPU
Interface
Data register
Status register
F
I/O
device
Data bus
I/O bus
Data valid
Data accepted
Address bus
I/O read
I/O write
Read data register
Check flag bit
Read status register
Transfer data to memory
Continue with program
Flag
Operation complete?
= 0
= 1
yes
no

## Slide 12: Interrupt-initiated I/O
An alternative to the CPU constantly monitoring the flag is to let the interface inform the computer when it is ready to transfer data.
While the CPU is running a program, it does not check the flag.
However, when the flag is set, the computer is momentarily interrupted from proceeding with current program and is informed of the fact that the flag has been set.
The CPU deviates from what it is doing to take care of the input or output transfer.
After the transfer is completed, the computer returns to the previous program to continue what it was doing before the interrupt.

## Slide 13: Priority Interrupt
Section - 3

## Slide 14: Priority Interrupt (Daisy-Chaining Technique)
Determines which interrupt is to be served first when two or more requests are made simultaneously
Also determines which interrupts are permitted to interrupt the computer while another is being serviced.
Higher priority interrupts can make requests while servicing a lower priority interrupt.
Device 1
PI
PO
Device 2
PI
PO
Device 3
PI
PO
CPU
INT
INTACK
VAD 1
VAD 2
VAD 3
Processor data bus
Interrupt request
Interrupt acknowledge
To next
device

## Slide 15: DMA (Direct Memory Access)
Section - 4

## Slide 16: DMA (Direct Memory Access)
The transfer of data between a fast storage device such as magnetic disk and memory is often limited by the speed of the CPU.
Removing the CPU from the path and letting the peripheral device manage the memory buses directly would improve the speed of transfer.
This transfer technique is called direct memory access (DMA).
During DMA, CPU is idle and has no control of the memory buses.
A DMA controller takes over the buses to manage the transfer directly between the I/O device and memory.
BR
BG
ABUS
DBUS
RD
WR
CPU
Bus request
Bus granted
Address bus
Data bus
Read
Write
High-impedance (disabled) when BG is enabled

## Slide 17: DMA Controller
DMA Controller
DMA controller - Interface which allows I/O transfer directly between Memory and Device, freeing CPU for other tasks
CPU initializes DMA Controller by sending memory address and the block size (number of words).
BR
BG
DS
RS
RD
WR
Control logic
Bus request
Bus grant
Read
Write
Interrupt
Register select
DMA Select
Interrupt
Data bus buffers
Data bus
Internal Bus
Address bus buffers
Address register
Word count register
Control register
Address bus
DMA Acknowledge
DMA Request
to I/O device

## Slide 18: Input-Output Processor (IOP)
Section - 5

## Slide 19: Input-Output Processor (IOP)
Memory Unit
Central Processing Unit (CPU)
Input-Output Processor
PD
PD
PD
PD
Peripheral Device
Memory Bus
I/O Bus

## Slide 20
Send instruction to test IOP path
Transfer status word to memory location
If status OK, send start I/O instruction to IOP
Access memory for IOP program
CPU continues with another program
Conduct I/O transfers using DMA; prepare status report
I/O transfer completed; interrupt CPU
Request IOP status
Transfer status word to memory location
Check status word for correct transfer
CPU operations
IOP operations
Continue
CPU – IOP Communication